## Slide 1
CONTRACTOR SAFETY BRIEFING // FIELD CONTROLS
DEEP EXCAVATION,
SHORING & DEWATERING
Permit discipline, monitoring, audit controls and flooded-collapse readiness.
CONSTRUCTION • TEMPORARY WORKS • DEWATERING TEAMS
SECTION A–A
GWL
EXCAVATION > 5.0 M
SITE SAFETY UAE
ADOSH-SF v4.0 (July 2024) aligned

## Slide 2
SAFETY SYSTEM BRIEFING // SHEET-PILE INTERFACE
Deep excavations fail
at the interfaces
A permit to work stays valid only while ground, water and temporary works all perform within approved limits.
01
GROUND
Soil conditions, surcharge and vibration affect every support decision.
02
WATER
Drawdown, inflow and discharge control can change ground behaviour rapidly.
03
TEMPORARY WORKS
Sheet piles, walings, struts and anchors must remain at the approved stage.
NO-GO
If any one of the three systems moves outside its approved limits, the permit is no longer valid.
SECTION A–A
GWL
EXCAVATION > 5.0 M
Source framework: ADOSH-SF CoP 29.0 Excavation Work • CoP 21.0 Permit to Work Systems
SITE SAFETY UAE
02

## Slide 3
MUNICIPALITY & DISCHARGE CONTROL
Dewatering approval is plot-specific
Confirm the plot jurisdiction, receiving asset owner and approved route before any pump runs.
01 / EMIRATE OF ABU DHABI
Abu Dhabi
Approval pathway: ADM/DMT approvals with the relevant environmental and receiving-asset controls.
Contractor control: maintain permit and testing evidence. Effluent must be free of solids, pollutants and oil.
02 / EMIRATE OF DUBAI
Dubai
Approval pathway: authority depends on plot and receiver — DDA, municipality, master developer or free zone.
Contractor control: the DDA NOC permits the approved storm-network or temporary-lagoon route for that development area.
03 / EMIRATE OF SHARJAH
Sharjah
Approval pathway: written, project-specific confirmation through Sharjah Municipality and the receiving-asset owner.
Contractor control: no public standalone procedure verified — treat discharge as prohibited until route and conditions are approved.
NO-GO // VERIFY AT EACH PTW ISSUE AND ROUTE CHANGE
No approval, no pumping. The permit must state the exact plot, route, receiving asset, duration and water-quality conditions.
Sources: ADM Circular 001/2024 • DDA Dewatering NOC • Build in Dubai • Sharjah Municipality
SITE SAFETY UAE
03

## Slide 4
DEWATERING RELEASE GATE // APPROVED DISCHARGE ROUTE
Control the water
before work starts
Confirm the NOC, discharge receiver and current drawing before the excavation/dewatering PTW is issued.
01
APPROVED DESIGN
Method, target drawdown, pumping rate, duration, standby capacity and treatment arrangement.
02
ROUTE DRAWING
Key plan, protected pipe route, discharge point and system layout verified at the work face.
03
VALID AUTHORITY NOC
Approval must match the exact plot, receiver, operating period and issuing authority.
04
CLEAN-EFFLUENT EVIDENCE
Silt, oil and pollutant controls installed; required sampling and testing records are available.
NO APPROVAL, NO PUMPING
A missing or mismatched NOC stops the permit — it is not a paperwork defect to close out later.
DISCHARGE ROUTE
SUMP
TREAT
APPROVED RECEIVER
NOC-DEFINED ROUTE
Route, receiver and duration on the NOC must match the drawing held at the work face.
Source framework: ADM Circular 001/2024 • DDA Dewatering NOC • ADOSH-SF CoP 29.0
SITE SAFETY UAE
04

## Slide 5
MONITORING PLAN // FIELD VERIFICATION
Monitor the ground–water–
support system
Instrument the design assumptions, then combine readings with competent-person visual inspections.
01
WALL MOVEMENT
Inclinometers, survey prisms and total-station readings reveal lateral deflection and rotation of sheet piles or shoring walls.
02
GROUNDWATER
Piezometers and observation wells track drawdown, pore pressure, inflow and off-site groundwater response.
03
SUPPORT LOADS
Strut, anchor and hydraulic-pressure measurements confirm temporary works perform within the approved design envelope.
04
VISIBLE DISTRESS
Settlement points, crack mapping, seepage checks and daily inspection identify conditions instruments may not capture.
INSTRUMENTATION
INCL
PIEZO
SUPPORT STAGE
Instrument type, location, baseline and trigger levels are set by the geotechnical and temporary-works designers.
Source framework: ADOSH-SF CoP 29.0 — Excavation Work
SITE SAFETY UAE
05

## Slide 6
MONITORING GOVERNANCE // DESIGN-APPROVED TRIGGER LEVELS ONLY
Turn readings into decisions
Thresholds, reading frequency and response authority come from the geotechnical and temporary-works design — never from generic millimetre limits.
GREEN // CONTINUE ROUTINE CHECKS
Within envelope
Readings and rate of change remain within the approved design envelope. Maintain the planned frequency and keep records current.
ALERT // INVESTIGATE AND CONTROL
Trend approaching
A trend approaches a limit or a reading is anomalous. Verify the reading, inspect the work face and increase monitoring frequency.
ACTION / ALARM // SUSPEND PTW
Limit exceeded
A limit is exceeded, change accelerates or warning signs indicate instability. Stop affected work; isolate, inspect, evacuate if required and obtain engineer direction.
NEVER COPY GENERIC LIMITS
Instrument thresholds and response authority are project-specific and must be issued by the designer before monitoring starts.
Source framework: ADOSH-SF CoP 29.0 Excavation Work • CoP 21.0 Permit to Work Systems
SITE SAFETY UAE
06

## Slide 7
CONTRACTOR AUDIT RELEASE // PERMIT & TEMPORARY WORKS
Audit the permit and
temporary works first
Verify at the work face before personnel enter, before each shift, and before the next excavation stage.
01
PTW & LINKED CONTROLS
Current excavation PTW, utility clearance and applicable isolation / lift / confined-space certificates are cross-referenced.
02
APPROVED SUPPORT STAGE
Installed sheet piles, walings, struts and anchors match the approved drawing and construction sequence.
03
INSPECTION & CONDITION
Competent-person inspection confirms no damage, displacement, seepage, adverse movement or unauthorised alteration.
04
SURCHARGE & PLANT
Spoil, cranes, rigs and vehicles remain outside the engineer-defined edge and loading limits.
EVIDENCE AT WORK FACE
VALID PERMIT AT WORK FACE
CURRENT DRAWING & RELEASE RECORD
DAILY / PRE-SHIFT INSPECTION
EXCLUSION ZONE VERIFIED
STOP WORK → SECURE / EXCLUDE → NOTIFY TWC → ENGINEER RELEASE
Do not release the area if installed temporary works differ from the authorised stage.
Source framework: ADOSH-SF CoP 29.0 Excavation Work • CoP 21.0 Permit to Work Systems
SITE SAFETY UAE
07

## Slide 8
CONTRACTOR AUDIT // DEWATERING FIELD VIEW
Dewatering must
stay controlled
Inspect the system as a continuous safety barrier, not as a pump-and-hose installation.
01
PUMP RESILIENCE
Duty and tested standby pumps, independent emergency power and adequate fuel are ready for every shift.
02
PERFORMANCE LOG
Water level, flow, runtime, pressure/current and groundwater response are recorded and reviewed against trigger levels.
03
PROTECTED ROUTES
Hoses, headers and electrical cables are secured, protected from plant and kept clear of access and rescue routes.
04
CLEAN DISCHARGE
Treatment, silt/oil control and required testing verify compliance with the approved receiving route and permit conditions.
STOP WORK
Rising water, pump failure, uncontrolled seepage or an unapproved discharge route requires immediate escalation and PTW review.
SYSTEM BARRIER
DUTY PUMP
STANDBY PUMP
EMERGENCY POWER
TREATMENT
APPROVED RECEIVER
Safe only when pumping, ground response and discharge remain controlled together.
Source framework: ADM Circular 001/2024 • DDA Dewatering NOC • ADOSH-SF CoP 29.0
SITE SAFETY UAE
08

## Slide 9
EMERGENCY RESPONSE / LIFE SAFETY // NO SPONTANEOUS RESCUE
Flooded collapse:
the first minute
Activate the incident plan — protect people before assets.
01
RAISE ALARM & STOP WORK
Stop excavation, lifting, pile driving and vehicle movement. Stop entry immediately.
02
EVACUATE & ACCOUNT
Clear the excavation and collapse zone by the safe route; complete a rapid head count.
03
CORDON & NOTIFY
Establish exclusion control and alert Incident Command, emergency services, temporary works and dewatering leads.
04
STABILISE — DO NOT ENTER
Assess wall movement, water rise, electricity and atmosphere before any planned rescue action.
NO SPONTANEOUS RESCUE
Do not send rescuers into flooded or unstable ground without a competent rescue lead and an engineering go/no-go decision.
TIMELINE
0–60 SEC — ALARM
1–3 MIN — EVACUATE
3–10 MIN — CORDON
10 MIN+ — ASSESS
Every action below is taken from outside the collapse zone.
Source framework: ADOSH-SF CoP 21.0 • Site emergency and rescue plan
SITE SAFETY UAE
09

## Slide 10
FLOODED COLLAPSE RESCUE PRINCIPLE // STABILITY IS LIFE SAFETY
Stabilise before you rescue
The first objective is to prevent additional casualties. Control hazards first, then use the recovery method the plan and rescue capability support.
01 / FREEZE THE HAZARDS
Control first
Stop plant, lifting and vibration; control water and electrical risks from a safe location; assess wall movement and atmosphere.
02 / CHOOSE NON-ENTRY FIRST
Non-entry recovery
Use remote accountability, safe-edge retrieval or a verified rescue platform whenever that can recover the casualty without exposing rescuers.
03 / RECOVER ONLY BY THE PLAN
Planned entry
Entry rescue needs Incident Command, a competent rescue lead, engineering go/no-go confirmation, suitable equipment and protected access.
NO-GO
Never improvise personnel lifting with cranes or excavators, and never send untrained rescuers into flooded or unstable ground.
Source framework: ADOSH-SF CoP 21.0 Permit to Work Systems • Project emergency and rescue plan
SITE SAFETY UAE
10

## Slide 11
CONTINUOUS EXCAVATION / PTW CONTROL
Shift handover revalidates the safety case
PTW: one shift or 12 hours — whichever is shorter.
OUTGOING SHIFT // INSPECT & RECORD
Record the state
The Permit Holder records support stage, monitoring trend, groundwater level, pumps, isolations, SIMOPS and outstanding defects.
FORMAL HANDOVER // REVALIDATE AT SITE
Verify on the ground
The incoming Authorized Person and Permit Holder complete a physical inspection and confirm the controls remain suitable.
INCOMING SHIFT // BRIEF & RESTART
Brief, then restart
The new work party is briefed in a common language, signs its understanding, then recommences only under the valid PTW.
01 TEMPORARY WORKS
Support configuration, inspection result, movement readings, restrictions and engineer instructions.
02 DEWATERING
Water level, duty/standby pump condition, power/fuel, discharge status and alarms.
03 PERMIT INTERFACES
Live permits, isolations, utility controls, lifting/plant activity and contractor SIMOPS.
04 EMERGENCY READINESS
Rescue team, access route, equipment, communications, weather and flood-response status.
REISSUE // CoP 21.0 REVALIDATION & MANAGEMENT OF CHANGE
Changed scope or conditions revoke the PTW. Stop work, reassess the risk and issue a new permit with the revised controls.
Source: ADOSH-SF CoP 21.0 — Permit to Work Systems, Version 4.0
SITE SAFETY UAE
11

## Slide 12
FIELD SAFETY COMMAND // CONTRACTOR NON-NEGOTIABLES
Four rules that never flex
These controls apply to every work party, every shift and every excavation stage.
01 STOP WORK WHEN CONDITIONS CHANGE
Rising water, movement, adverse gas testing or a monitoring Action/Alarm condition changes the safety case.
SECURE THE AREA → NOTIFY SUPERVISION → REVIEW PTW
02 NEVER ALTER TEMPORARY WORKS
Do not remove, loosen, relocate or load sheet piles, walings, struts, anchors or edge controls without written authority.
STOP THE TASK → CONTACT TEMPORARY WORKS → OBTAIN RELEASE
03 NEVER DISCHARGE WITHOUT APPROVAL
Groundwater discharge requires a route-specific approval, compliant treatment controls and the required verification records.
NO APPROVAL → NO PUMPING → NO DISCHARGE
04 NEVER IMPROVISE RESCUE ENTRY
Flooded or unstable excavations present secondary-collapse, electrical and atmospheric risks to unplanned rescuers.
RAISE ALARM → CORDON AREA → USE RESCUE PLAN
ESCALATE EARLY // PERMIT HOLDER → AUTHORIZED PERSON → TW / DEWATERING LEAD
The safest intervention is the one made before movement, flooding or instability accelerates.
Source framework: ADOSH-SF CoP 21.0 • CoP 29.0 • approved project emergency plan
SITE SAFETY UAE
12

## Slide 13
CLOSEOUT / FIELD DISCIPLINE
Brief. Verify. Record. Escalate.
Four actions before work continues — the control system works only when every work party applies it at the excavation face, on every shift.
01 / BRIEF
Brief
Confirm the work scope, active hazards, alarm signals, emergency route and stop-work triggers in a language the crew understands.
02 / VERIFY
Verify
Check permits, temporary works, water control, monitoring, access and rescue readiness at the work face.
03 / RECORD
Record
Capture inspections, readings, pump status, permits, NOCs, defects and corrective actions in the controlled project log.
04 / ESCALATE
Escalate
Stop early and refer changing conditions to the Permit Authority, temporary-works and dewatering leads.
CREW COMMITMENT
If the ground, water or support condition changes, stop work and make the safety case valid again before restarting.
Protect people first • Protect the temporary works • Protect the ground and water system
SITE SAFETY UAE
13

## Slide 14
REFERENCE REGISTER // SOURCE FRAMEWORK
Verify the current issued version
Confirm the project jurisdiction, receiving asset owner and authority conditions before work starts.
01 / ABU DHABI HSE — PRIMARY WORK CONTROL
ADOSH-SF CoP 29.0 — Excavation Work
Ground conditions, support systems, dewatering, competent-person inspection and deep-excavation atmospheric controls.
02 / ABU DHABI HSE — PERMIT CONTROL
ADOSH-SF CoP 21.0 — Permit to Work Systems
PTW issue, shift duration, revalidation, formal handover, SIMOPS, management of change and emergency suspension.
03 / ABU DHABI MUNICIPALITY — DISCHARGE CONTROL
ADM Circular 001/2024 — Dewatering Requirements
Site dewatering approvals, clean-effluent and testing evidence, discharge responsibilities and prohibited releases.
04 / DUBAI DEVELOPMENT AUTHORITY — PLOT NOC
DDA Dewatering NOC
Approval for underground-water discharge to an approved storm-water network or temporary lagoon in the relevant DDA area.
05 / DUBAI MUNICIPALITY CONTEXT — RECEIVING ROUTE
Build in Dubai — Service 430
Municipal NOC context for groundwater and wastewater discharge to sea, creek or canals; confirm live service requirements.
06 / SHARJAH — NO ASSUMED ROUTE
Sharjah Municipality — Written Direction
Obtain project-specific written confirmation of the receiver, route, conditions, testing and permit/NOC process before discharge.
VERIFY
Keep current permits, drawings, test results and authority correspondence at the work face. An approval is valid only for the stated plot, receiver, route, duration and water-quality conditions.
Reference portals: ADPHC • DMT-ADM • Dubai Development Authority • Build in Dubai • Sharjah Municipality
SITE SAFETY UAE
14